Sample from system
Construct utility
Model
Utility multidimensional surface
(Objective function)
Search
Experimental constraints
y_1
y_2
y_n
...
y_\mu
\sigma
c_x
u(x) = ||\sigma || \cdot c_x
x^* = \arg \max_{x} u(x)
y^* = f(x^*)

---
Search
Sample from system
Construct utility
Control surface
Utility surface
Model
Transition
Uncertainty
Exploration constraints
Operating constraints
\hat {y_}
|| \hat \sigma ||
c_x
w
u(x)
x^* = \arg \max_{x} u(x)
Train model
\dot m
T_1
T_2
Q_1
x^*
||\eta||

---
\eta(x) = \frac{1}{n_c+ |T_2-20|} + \frac{1}{n_c+|T_3-25|}
x
\hat y
y_{opt}
s=|| x_1 - x_2 ||_{L}

---
Utility surface
Exploration
Exploitation

---
\dot m
T_2
Q_1 = \dot m k_1 (T_2 - T_1)
T_3
Q_2 = \dot m k_2 (T_3 - T_2)
k_i = rand [0.5, 3]
Let, T_2 = 20 ^ \circ , \ T_3 = 25^ \circ
Given \ f(x)
constants, \dot m , T_1
x=(Q_1, Q_2)
y= T_2 , T_3
T_1
Q_1
Q_2

---
Exploration constraint